## Slide 1: ISDN PRODUCT GUIDE
emutel|Solo
arcatech Limited
Unit 402 LEO Ballinderry Road
Lisburn
Northern Ireland
BT28 2QA
Tel: +44 (0)28 9267 7204
Fax: +44 (0)28 9260 5353
sales@arcatech.com
www.arcatech.com

## Slide 2: Presentation Content
Solutions from arcatech Limited
Who is the emutel range used by
emutel|Solo features
Summary of features
Typical Applications
Other Products available from arcatech

## Slide 3: Solutions from arcatech Limited
ISDN
POTS
V5
xDSL
VoIP
Solo
Horizon
Symphony
Duo
Maestro
Harmony
Harmony

## Slide 4: Typical Customers

## Slide 5
The emutel range is used by
Developers
  ISDN
  xDSL
  VoIP
Production Line Testing
TE equipment
  Modems
  SIP/H.323 Gateway
Repair Houses
Confirm operation
For ISDN Network provision
Exhibitions/Shows
  Teaching facilities
  Labs

## Slide 6
A
B
emutel|Solo – 2 Port Basic Rate ISDN Network Simulator

## Slide 7
BRI Ports
2 Ports, each software switchable between BRI-S and BRI-U
BRI Interface Power
40V, 1W Normal and Restricted on BRI-S
55V, 1.5W Normal and Sealing on BRI-U
Network Variants
Support for ETSI, N.America and NTT
D Channel Packets
X.25 on BRI1/BRI2
100 logical calls in DCE mode
P-P / P-MP
Point-to-point or point-to-multipoint modes can be selected
Unit Features

## Slide 8
Semi-permanent connection (Leased Line)
Semi-permanent/nailed up IDSL connection on BRI B and D channels (144K
connection)
B Channel Delay
0-750ms delay on Port 1, B1 and B2 independently
Telephone no. setup
Allows telephone numbers to be setup for the various ports
Also allows different numbering schemes to be used (i.e. MSN, normal, DDI &
auxiliary)
Test Tones
Dial, Busy, Error, Ring, and Custom Tone 300Hz-3400Hz @ +3dBm to -26dBm
Unit Features

## Slide 9
Port Indicators
P (Physical), D(Datalink), S/U operation and port power status, B channel status
Internal battery
An internal rechargeable battery to power the unit
Universal PSU (110/240 V)
Auto detecting PSU - no changes required to alter voltage input, can be used in
different countries
Unit Features

## Slide 10
Summary of Features

## Slide 11: Typical Application
In this example, an emutel|Solo is providing a network interface to verify the operation of a piece of customers equipment.
ISDN Telephone
ISDN Telephone
ISDN PBX
Controlling PC

## Slide 12: Other products available from arcatech
emutel|Harmony
VoIP
ISDN
FXO
FXS
emutel|Symphony
FXS
ISDN
emutel|Duo
ISDN
arcaplex|Horizon
Multiplexer
ISDN
FXS
arcareach|Sigma
BRI-S bus extender
emutel|Maestro
xDSL

## Slide 13
emutel|Harmony
PESQ
Composer
Conductor
Events &
Statistics
Integrated VoIP & TDM Test Platform
High Port Density
VoIP, BRI, PRI, LAN, FXO, FXS
ETSI, North American, NTT, SIP, H.323
Quality of Service (PESQ)
Protocol Analysis
Call Generation
Call Termination
Network Simulation

## Slide 14: emutel|Symphony
Analyser
Connection configuration
Medium Port Density
ISDN support, both BRI and PRI
Analogue FXS support
Support for Network Variants
Protocol Analyser
Remote configuration
Windows Application driven

## Slide 15: emutel|Duo
Low Port Density
ISDN support, both BRI and PRI
Support for Network Variants
Protocol Analyser
Remote configuration
Windows Application driven
Analyser
Connection configuration

## Slide 16: arcaplex|Horizon
PRI – ISDN/Analogue Multiplexer
Allows an E1 or T1 Network to be used with up to
16xBRI or 32xAnalogue phones
PRI network port allows for connection to another
Horizon or PRI TE equipment
CLI Interface

## Slide 17: arcareach|Sigma
Converts BRI-S to BRI-U
When used in conjunction with an NT-1
enabling the extension of an S-bus up to 5.5km

## Slide 18: emutel|Maestro
Support for
ADSL (Annex A,B,C)
SHDSL
VDSL
Data Sources
ATM
Ethernet
Internal Web server
Windows Application
Configuration of Bandwidth,
upstream and downstream
Windows Application

## Slide 19: The End